Sample Preparation

clean – shells only
place sample into a 20 mL beaker marked with sample ID
rinse, sonicate as needed and drain
break shell(s), if they float, if any contamination is visible within whorls
or if the interior cannot otherwise be inspected
pipette if necessary to avoid losing material
repeat until drained UPW is clear and all sample surfaces are visible and clean
bleach 4 hr in 10 mL 3% H2O2 @ 60 °C
cover beaker tightly with foil cap to prevent excessive evaporation
the cap also helps keep the beaker from jamming in the hot block
decant & discard supernatant
rinse twice, pipette off as much water as possible
dry on heat block under foil tent @ 60..80 °C
weigh sample; select test sample of up to 20 mg

leach - non-powdered carbonate samples only
determine amount of sample to leach
ideal "leach mass" is 30..50% of initial test sample mass
ideal post-leach mass is 8.3..9 mg pure carbonate
more is needed if non-carbonate material is present in sample
minimum post-leach test sample mass is 1.8 mg pure carbonate
determine volume and concentration of acid required for leach step
if leach mass > 1.8 mg
"leaching acid" = 0.20 mL of 0.1 N HCl per mg of leach mass
if leach mass ≤ 1.8 mg
“leaching acid” = 2.0 mL of 0.01 N HCl per mg of leach mass
leach 30 min in "leaching acid" @ 80 °C
( CaCO3 + 2HCl → Ca+ + 2Cl- + H2O + CO2 )
adjust small pipette to deliver metered quantity
inject metered quantity of “leaching acid” into sample
add UPW as needed to raise volume to 5 mL
ensure entire sample is submerged
cover beaker with foil cap
place beaker into hot block at 80 °C for ≥ 30 min
leach is complete when pH > 4
rinse twice, pipette off as much water as possible
dry on heat block under foil tent @ 60..80 °C
crush to ≤ 0.3 mm powder (normalizes acid digestion)

weigh – blanks (C1) and secondary standards (C2) processing starts here
nominal sample size is 6.9..8.7 mg per aliquot
place test sample into Exetainer vial and secure the septum cap

evacuate
tighten vial cap, dust and lube/seal septum with a drop of UPW
load vial onto needle port of vacuum line under positive He pressure
evacuate vial to ≤ 1e-4 Torr
pressurize vial with He to > atmospheric pressure (~720..800 torr)
this step prevents water from being drawn into vacuum line or vial
make sure septum/needle is sealed with water, then remove vial from needle port
mark vial top with Sharpie marker dot to indicate it has been evacuated

lube/seal septum with a drop of UPW
use a clean syringe to withdraw ~6 cc (for a nominal 1-aliquot sample) of He from vial
Some water will be drawn into the needle as it is removed from the septum. This	is normal. A small amount of water may be drawn into the vial. This is ok,	too. Air must not be drawn into the vial.

digest sample 20..40 min in ~0.8..1 mL degassed 85% H3PO4 @ 80 °C
Note: 0.8 mL is enough acid for any size of sample. Less than 0.0011 mL acid is consumed per mg of sample; e.g., given a 25 mg sample, any amount of acid over 0.028 mL is excess.

Acid Digestion reaction:
3Ca(CO3) + 2H3PO4 → Ca3(PO4)2 + 3H2O + 3CO2

remove needle and draw into syringe ~1 mL acid per sample to be digested
attach needle and expel any air from syringe
lube/seal septum with a drop of UPW
inject 0.8 to 1.0 mL H3PO4 into the vial
do not allow any air to enter the vial
place vial into hot block at 80 °C
periodically check reaction progress (every 10..20 minutes)
“roll” acid all over the vial wall
to make sure any sample material there is digested, too
avoid getting acid on septum
reaction is complete when liquid is clear and not bubbling

sample is ready for carbon extraction and graphitization